| Hazard | Effect | Control measures | Residual risk |
| --- | --- | --- | --- |
| Electricity | Electric shock | Check condition of lead and plug before use. Use 110v or battery tools or RCD where practicable. Check for hidden/buried cables before drilling etc. Do not work where water is present without specialist advice. Qualified person to test all portable electrical hand tools at least annually. | Low |
| Flammable/explosive atmosphere | Fire/Explosion | Do not use heat generating equipment without Hot Work Permit. Do not work near flammables, compressed gases, in explosive atmospheres or confined spaces without specialist advice. Check with Clerk of Works before using flammable fuel or gas driven equipment. | Low |
| Moving parts | Entanglement | Loose clothing, jewellery and long hair to be kept clear of moving parts. Use guards where appropriate. | Low |
| Flying debris, swarf etc. | Eye, hand or facial injury | Use protective eyewear or face shield. Use guards where appropriate. Wear protective gloves where appropriate. Advise nearby persons of hazard. Isolate area with barriers, tape etc. where necessary. | Low |
| Noise | Hearing damage | Wear hearing protection if above 80dB(A) or if uncomfortably loud (request assessment if in doubt). Advise nearby persons of hazard. Supervisors should inform users of risks from noise. | Low/moderate |
| Vibration | Hand/Arm Vibration Syndrome (HAVS) Carpal Tunnel Syndrome | Select power tools with lowest vibration levels. Minimise the time individuals use the equipment (e.g. job rotation). Restrict use of vibration inducing tools to recommended times (see Departmental guidance, manufacturer’s information, local risk assessment or label on equipment/ box). Ensure tools are properly stored, maintained and used according to manufacturer’s instructions. Supervisors should inform users of risks from vibration. Arrange health surveillance for those identified at risk from vibration. | Low/moderate |

| Hazard | Effect | Control measures | Residual risk |
| --- | --- | --- | --- |
| Ergonomic | Musculo-skeletal injury | Ensure there is adequate room to do the job. Minimise the time individuals use heavy equipment (e.g. job rotation). Use jigs and suspension systems to assist the handling of heavy equipment (e.g. large grinders). Wear safety footwear unless feet protected by other means (e.g. sitting at a bench). | Low/moderate |
| Slips, trips and falls | Minor injury Major injury Fatal injury | Ensure work area is free (as is practicable) from trailing cables, tools, materials, debris and spills. All work should be from a suitable and stable work platform. The use of ladders restricted to trained users and must be cleared with supervisor. | Moderate Low Low |
| Dust | Respiratory illness Reduced visibility Skin irritation | Use a dust mask (check for fit). Increase ventilation to work area (e.g. open windows, temporary extract etc.) Wear close-fitting safety goggles. Stop working if visibility is noticeably reduced. Wear suitable protective clothing (especially gloves). Clean work area regularly (e.g. sweep, vacuum, wash down). | Low |
| Air line detaching or bursting | Eye/face injury Distraction | Check condition and connections of air-line before use. Ensure air-line is not on a traffic route (pedestrian or vehicular). | Low |
| Tool jamming or binding | Wrist/hand injury | Check tool is appropriate for the job and used in accordance with manufacturer’s instructions. Trained operators only (or under strict supervision). Ensure tools are maintained according to manufacturer’s instructions. | Low/moderate |
| Inappropriate use | All of above | Check tool is appropriate for the job and used in accordance with manufacturer’s instructions. Users shall be trained in the correct use of portable tools. Inexperienced power tools users should be supervised or observed when first using an unfamiliar item of equipment or in an unfamiliar environment. Power tools should be securely stored when not in use. | Low/moderate |

Signature to confirm that this is a suitable and sufficient assessment of risk and that stated control measures are in place and will be reviewed.

| Name of Assessor Email: | Signature | Date |
| --- | --- | --- |
| Name of Supervisor | Signature | Date |

| Local Safety Coordinator | Signature | Date |
| --- | --- | --- |
| Departmental Safety Office | Signature | Date |

| Additional Users | Signature | Date |
| --- | --- | --- |